## Slide 1: Hardware Components

## Slide 2: The Motherboard
All these devices connect to a main circuit board called a motherboard

## Slide 4
CPU
CPU performs all types of data processing operations
Fetches, decodes and executes instructions stored in RAM
Two lines of chips manufactured by Intel and AMD eg Core i5 and Ryzen 5.

## Slide 7
Chipset
Orchestrates the flow of data between key components of the computer
  communication between the CPU, RAM, storage and other peripherals
  Also controls external buses, memory cache and some peripherals. A CPU is unable to function without the chipset timing
Designed by Intel and AMD

## Slide 8: North Bridge
The northbridge is also known as a front side bus
A high-speed path between the CPU, RAM and video card

## Slide 9: South Bridge
Communicates with all the slow hardware devices
  SATA/ATA hard disk
  USB

## Slide 10: RAM
RAM is volatile, i.e. data stored in is lost when power is off
Two types
SRAM faster, doesn’t need to be refreshed
DRAM slower than SRAM and must be continually refreshed
Comes in SDRAM modules (DDR2, DDR3, DDR4 etc.

## Slide 13: Expansion Slots
A place on the motherboard where expansion cards can be inserted.
PCIe – PCI Express
Various sizes (X1 – X16)
X1 slower for audio/network card
X16 is fast for graphics card
x1
x4
x8
x16

## Slide 16: Video Card
Provides video capability
Allows a monitor to connect to PC
  VGA
  HDMI
  DVI
PCIe – PCI Express Slot
VGA
DVI

## Slide 17: Sound Card
Provides audio capability
Allows speaker systems to connect to computer
  3.5mm jack
  Sometimes digital SPDIF
PCIe – PCI Express Slot
3.5mm Jacks
SPDIF

## Slide 19: Power Supply
Provides power to motherboard and components
Mains power connects to power supply
Power supply distributes power to internal components
  hard drive
  motherboard
  cards in expansion slots
  Some usb devices

## Slide 20: BIOS
Basic Input Output System
Perform hardware initialization during the booting process
Loads a boot loader from a mass bootable hard drive which then starts the operating system
New UEFI replaces the old BIOS

## Slide 21: Hard Disk Drive
Also known as secondary storage
Acts like a filing cabinet
Stores files and applications
Connects via SATA or SAS
2.5-inch and 3.5-inch
Components include disk platter, actuator arm and read/write head

## Slide 23: Reading and Writing Data
Surface of the disk is divided into tracks and sectors
Bits of data are arranged into tracks
Tracks are divided into sectors
Each sector stores a fixed amount of data – eg 512 bytes

## Slide 25: Optical Drive
CD, DVD, Blu-ray
Reads disk with laser
Obsolete nowadays

## Slide 27: Reading Data
Data is written to the disk in 1 continuous track
Data is encoded in pits and lands
  Pit = 0
  Land = 1

## Slide 29: Memory Cards
Various Types
  SD
  Compact Flash
Can be up to 512GB

## Slide 30: External Hard Drives
Portable Hard Disk Drive
Plugs in via USB
Can be up to 1TB or more

## Slide 31: Flash Drives
Stores data on flash memory
Can be up to 512GB, sometimes more
Plugs in via USB

## Slide 32: Printers
Laser and Inkjet
Connect to PC via USB or wireless